Solid Waste Management Improvement Project

ADB Loan No.: 3067-UZB

PROJECT MANAGEMENT, IMPLEMENTATION AND SUPERVISION CONSULTANCY SERVICES

Contract No.: SUE/Maxsustrans/QCBS-Cons_1-2016-01

Environmental Monitoring Report

August - October 2017

CLIENT – IMPLEMENTING AGENCY

State Unitary Enterprise (SUE) “MAXSUSTRANS” (Tashkent, Uzbekistan)

LEAD CONSULTANT

H.P. Gauff Ingenieure GmbH & Co. KG-JBG (Germany)

in association with

ENG-INVEST Consulting Ltd. (Uzbekistan)

Environmental Monitoring Report

_________________________________________________________________

Project Number: 45366

Reporting period: August-October 2017

Loan Number: 3067-UZB

Republic of Uzbekistan:

Solid Waste Management Improvement Project

Financed by: Asian Development Bank

Prepared by H.P. Gauff Ingenieure GmbH & Co. KG – JBG- (Germany) and ENG-INVEST Consulting Ltd. (Uzbekistan) for “State Unitary Enterprise “Maxsustrans” and Tashkent Municipality and the Asian Development Bank.

ABBREVIATIONS

| ADB | Asian Development Bank |
| --- | --- |
| EA | Executing Agency |
| EHS | Environmental Health & Safety |
| EIA | Environmental Impact Assessment |
| EIP | Environmental Impact Permit |
| EMP | Environnemental Management Plan |
| ES | Environmental Specialist |
| GoU | Government of Uzbekistan |
| GRM | Grievance Redress Mechanism |
| IA | Implementing Agency |
| IEE | Initial Environmental Examination |
| LARP | Land Acquisition and Resettlement Plan |
| Maxsustrans | State Unitary Enterprise “Maxsustrans” |
| PIU | Project Implementation Unit |
| SCEEP | State Committee of the Republic of Uzbekistan of Ecology and Environment Protection |
| SLF | Sanitary Landfill Facility |
| SPS | Safeguard Policy Statement |
| SSEMP | Site-specific Environmental Management Plan |
| SWM | Solid waste management |
| SWMIP | Solid Waste Management Improvement Project |
| MSW | Municipal Solid Waste |

CONTENTS

1.	INTRODUCTION	6

1.1.	Project Background	6

1.2.	Project Objectives and Outputs	7

1.3.	Project Site Description	9

1.4.	Extent of the IEE Study	10

1.5.	ADB Policy	11

2.	PROJECT PROFILE	11

2.1.	Type, Category and Need	11

2.2.	Construction activities and project progress during the previous period.	12

3.	ENVIRONMENTAL ORGANISATION AND MANAGEMENT	13

3.1.	Organizational & Safeguard Aspects	13

3.2.	Project Organization and Stakeholders	13

3.3.	Agencies Involved in Investment Program Implementation	14

3.4.	Responsibilities for supervision of environmental matters	14

3.5.	Responsible for carrying out mitigation measures	15

3.6.	Relationships with Contractors, Owner, Lender, etc	15

3.7.	Responsible for carrying out monitoring measures	16

3.8.	Responsible for reporting	16

3.9.	Third Party Agency for EMP	17

3.10.	Grievance redresses mechanism (GRM)	17

4.	ENVIRONMENTAL SAFEGUARD COMPLIANCE	20

4.1.	Objectives of the Environmental Management Plan	20

4.2.	LARP implementation	21

4.3.	ADB Mission	22

4.4.	Communication	22

5.	Environmental Monitoring	23

5.1.	The Environmental Management System, site-specific environmental management plan (SSEMP) and work plans	23

5.2.	Site Inspections and Audit	23

5.3.	Non-Compliance Notices	23

5.4.	Corrective Action Plans	23

5.5.	Actions taken to reflect the findings of ADB mission	23

5.6.	Consultations and Complaints	24

6.	CONCLUSIONS AND ACTION PLAN FOR THE NEXT PERIOD	24

# INTRODUCTION

## Project Background

- The Government of Uzbekistan (GoU) has applied for a loan from the Asian Development Bank (ADB) for the development and improvement of Solid Waste Management (SWM) system of the capital city (Tashkent). The loan reference number is L3067-UZB: Solid Waste Management Improvement Project (SWMIP). The loan was signed between the Republic of Uzbekistan and Asian Development Bank (ADB) dated 27 February 2014 and Project Agreement dated 12 March 2014 signed between ADB, Tashkent City Municipality and the State Unitary Enterprise “MAXSUSTRANS”.

- The project was prepared to impact an improved urban environment and quality of life for the residents of Tashkent. The project will develop a sanitary landfill that meets international standards, rehabilitate transfer stations, and modernize the waste collection and transfer fleet. It will build capacity in waste management and help formulate a national strategy on solid waste management.

- The Government of Uzbekistan (GOU) seriously recognizes the need to develop and implement a national Solid Waste Management (SWM) strategy. Therefore, the GOU has requested support from ADB to address the SWM challenges. The proposed Project will contribute to sustainable urban development in Uzbekistan by: (i) modernizing SWM to provide continuous and reliable municipal services; (ii) promoting financial sustainability of municipal services through tariff rationalization and prudent financial management; (iii) supporting policy and institutional reforms for improved sanitation and environmental management; (iv) mitigating climate change through a major reduction of GHG emissions, and through compliance with international standards on waste minimization and material recycling; and through all these measures; (v) improving livability of cities.

- The volume of the existing dumpsite is exhausted and the original plan of the city was to extend its dumpsite operations to an adjacent lot of additional 30 hectares of area. Being fully aware of the inevitable environmental impacts through the extension of this practice, the city asked the national government for assistance in this matter. Based on these activities, the Cabinet of Ministers approved in summer 2012 the location of new dumpsite on 30 hectares of agricultural area for the utilization for waste management activities.

- GOU has already decided to start processing land allocation of a 30-hectare land plot immediately to the south of the existing Akhangaran dumpsite, on which to develop an interim dumpsite extension. This facility is designed to accommodate Tashkent’s municipal waste for the next - 7 years, and until the longer-term solution is operational. However, following discussions, the city is now planning to reposition this 30-hectare facility to 25-hectare to the east of the existing dumpsite, and also to upgrade this facility to a sanitary landfill facility, designed to internationally accepted standards of environmental protection.

- Last option of expansion of landfill to the east, it has the potential for progressive expansion to become a 250-hectare long-term regional landfill, which can serve Tashkent’s disposal needs for at least 50-years. In other words, this initial landfill actually is the first development phase of the much larger regional landfill, should this option be later selected by the city as the long-term disposal solution. Should the alternative long-term option be selected instead however, then this interim facility could be closed, or possibly could switch to serve the disposal needs of nearby communities. A conceptual design has been completed for the interim 25-hectare facility, which is naturally included as a component of the Project.

## Project Objectives and Outputs

- The overall objective is to provide an improved solid waste management (SWM) system in Tashkent, the capital city, to upgrade urban infrastructure and services. The project will develop a sanitary landfill that meets international standards, rehabilitate transfer stations, and modernize the waste collection and transfer fleet. It will build capacity in waste management and help formulate a national strategy on solid waste management.

- Given the current SWM practices, the option converting and allocating an area adjacent to the existing dumpsite to an engineered Sanitary Landfill was decided. The proposed sanitary landfill facility (SLF) concept will be based on the Best Environmental Practices (BEP) resulting to a state-of–the-art design consistent with international acceptable standards. This “stand alone” facility will drastically improve the SWM system (i.e. the handling and final disposal of MSW) with a possible integration capability for a long-solution to cover the entire Tashkent Oblast. The inclusion into the design of a multi-barrier system, leachate and gas collection systems will result in a significant reduction of anticipated impacts. Solid Waste Management Improvement Project (hereinafter called “Project”) is to contribute to the following issues:

Segregation of Municipal Solid Waste stream; Proper collection and dumping to appropriate sites Establishment of modern SWM systems Remediation of old 'truck and dump' practices in cities and regions

- Therefore, the project objective can be defined as follows:

Technical, economic and financial feasibility; Focus on testing least cost technical solutions based on international standards, Operate on the principles of waste minimization and material recycling To achieve efficient collection, transfer and disposal of residual waste that meet acceptable standards of environmental protection

- The Government of Uzbekistan has agreed for a loan from the Asian Development Bank (ADB) for the development and improvement of Solid Waste Management system of the capital city Tashkent. The Loan Agreement was signed on 27.02.2014 between the Republic of Uzbekistan and Asian Development Bank and the Project Agreement dated 12.03.2014 was signed between ADB, Tashkent City Municipality and the State Unitary Enterprise “MAXSUSTRANS”. The loan reference number is L3067-UZB: Solid Waste Management Improvement Project (SWMIP).

- The special Decree of Uzbekistan President No.PP-2255 about the implementation of SWMIP has been issued on 31.10.2014, which specified five years project implementation period (2014-2018) and total project cost - USD 92,25 mln., of which USD 69,0 mln. the loan funds from ADB and USD 23,25 mln. the contribution of SUE “Maxsustrans” and the GoU. The GoU contribution is provided as exemption of tax and customs duties in Uzbekistan for the amount of USD 5,82 mln.

- The GoU through it Implementing Agency (IA), the State Unitary Enterprise (SUE) “MAXSUSTRANS” utilizes part of this loan proceeds towards the cost of the contract for Consulting Services related to Project Management, Implementation and Supervision, supporting the Project Implementation Unit (PIU).

- The project was prepared to impact an improved urban environment and quality of life for the residents of Tashkent. The outcome will be improved SWM services and management in Tashkent with the following key outputs:

- Output 1 - Rehabilitated and expanded solid waste management (SWM) system in Tashkent. By the project completion it is expected that (i) rehabilitation of transfer stations and possible closure of an existing transfer station,2 (ii) 3 million tons of disposal capacity established with international environmental standards, and (iii) 1,950 tons per day of disposal and operational capacity established;

- Output 2 - Strengthened operational capacity. By the project completion it is expected that (i) at least 90% of households actively segregating waste at source, (ii) campaign to raise awareness will reach 90% of households on waste segregation with women households members’ participation, (iii) improved management and operations of Maxsustrans, including a 20% improvement (reduction) in cost per ton of waste disposal, and (iv) an IT-supported MSW collection system based on a geographic information system (GIS) database is implemented and 80% of trips monitored by the system is achieved.; and

- Output 3 - National SWM strategy. By 2016, a draft national SWM strategy prepared and submitted to the Government and ADB.

- There are two executing agencies (EAs) for the project – the Tashkent Municipality (Hokimiyat of Tashkent city) for the overall oversight and monitoring of Outputs 1 and 2 and State Committee of the Republic of Uzbekistan of Ecology and Environment Protection (SCEEP) for execution of Output 3–the national SWM strategy. Outputs 1 and 2 will be implemented by State Unitary Enterprise “MAXSUSTRANS”. A PIU was established within MAXSUSTRANS to support project implementation. This support will include project management, financial management, procurement, contract administration, safeguards implementation, construction and technical supervision, and monitoring and evaluation.

## Project Site Description

- The Akhangaran landfill is located approximately 35 km south of the center of Tashkent City in the Akhangaran district of Tashkent Province. The facility has been in use since 1967 and is currently handling the wastes collected from Tashkent city and partial from Chirchik. The proposed site for a modern Sanitary Landfill is located at the eastern side of the existing Akhangaran Landfill. The total area for Landfill will cover approximately 25 hectares of agricultural land.

- Visibly, the adjacent areas are irrigated agricultural areas predominantly characterized by undulating valleys. There are no residential areas or industrial facilities within a 3-4 kilometer radius. Farmers come primarily from villages located about 5 kilometers from the site. At the landfill area, there are established basic facilities such as a weighbridge, administrative building, a maintenance shed, security gate, and record-keeping shed. The area is connected to the main road, Highway P2 via an asphalt access road that leads directly to the landfill. The distance from the highway to the landfill area is about a kilometer. Aside from the typical agricultural vegetation being grown, the area is characterized by reeds often found along the boundaries of each plot. Common farm livestock is common in the area.

Figure 1 Location map of Akhangaran landfill

- Access to the site: Land acquisition for the expansion of existing landfill will not require construction of any additional access road to the site. This is visualized below on given image (Figure below). Access to land will be through already functioning road. Buffer zone for the SLF will be within the acquired land plots.

* Yellow line is border of existing landfill; blue line is border of expansion

Figure 2 proposed Akhangaran landfill expansion

Figure 3 Map of acquired land plot and irrigation canal

## Extent of the IEE Study

- The IEE report (was prepared in May 2013) covers the general environmental profile of the project and includes an overview of the potential environmental impacts and their magnitude on physical, ecological, economic, and social and cultural resources within the subproject’s influence area during design, construction, and operation stages. An Environmental Management Plan (EMP) is also proposed as part of this report which includes mitigation measures for significant environmental impacts during implementation of the Project, environmental monitoring program, and the responsible entities for mitigation and monitoring.

## ADB Policy

- ADB requires the consideration of environmental issues in all aspects of ADB’s operations, and the requirements for Environmental Assessment are described in ADB’s SPS (2009). This states that ADB requires environmental assessment of all project loans, program loans, sector loans, sector development program loans, loans involving financial intermediaries, and private sector loans.

- Screening and Categorization. The nature of the environmental assessment required for a project depends on the significance of its environmental impacts, which are related to the type and location of the project, the sensitivity, scale, nature and magnitude of its potential impacts, and the availability of cost-effective mitigation measures. Projects are screened for their expected environmental impact are assigned to one of the following four categories:

- Category A. Projects could have significant adverse environmental impacts. An EIA is required to address significant impacts.

- Category B. Projects could have some adverse environmental impacts, but of lesser degree or significance than those in category A. An IEE is required to determine whether significant environmental impacts warranting an EIA are likely. If an EIA is not needed, the IEE is regarded as the final environmental assessment report.

- Category C. Projects are unlikely to have adverse environmental impacts. No EIA or IEE is required, although environmental implications are reviewed.

- Category FI. Projects involve a credit line through a financial intermediary or an equity investment in a financial intermediary. The financial intermediary must apply an environmental management system, unless all Projects will result in insignificant impacts.

- Environmental Management Plan. An EMP which addresses the potential impacts and risks identified by the environmental assessment shall be prepared. The level of detail and complexity of the EMP and the priority of the identified measures and actions will be commensurate with the Project’s impact and risks.

# PROJECT PROFILE

## Type, Category and Need

- Type. This is a solid waste management subproject intended to improve the current situation in Tashkent in terms of providing a disposal area, improving the collection system, and raising the awareness of the community of their responsibility to place their waste at collection points, and to segregate waste that is suitable for recycling.

- Category. Environmental examination indicates the proposed subproject falls within ADB’s environmental Category B projects. The Project components will only have small scale, localized impacts on the environment, and can be mitigated. Under ADB procedures such projects require an IEE to identify and mitigate the impacts, and to determine whether further study or a more detailed EIA may be required.

## Construction activities and project progress during the previous period

- Based on data available at the ADB web site as of end of August 2017, the total disbursed amount reached USD 5.304.870, that corresponds to 7,7% from the total loan amount. These funds were initially used for the supply of goods, PIU maintenance, payment for services of both individual consultants and consultant firms.

- To be mentioned that to the Commencement Date of the Consultant the IA has arranged the following procurement packages:

GOODS:

- SUE/Maxsustrans/ICB-G3-2016-01 - Waste collection bins 750 l and 1100 l, 2 Lots (current status: delivery was completed. Upon request of SUE “Maxsustrans” this Contract can be extended till the end of this year by delivery of additional 30% waste collection bins)

- SUE/Maxsustrans/ICB-G2-2016-02 - Waste Collection Trucks and Transfer trucks; Trailers and Containers (3 lots) (current status: bid evaluation in progress)

- SUE/Maxsustrans/ICB-G4-2017-04 - Office equipment for PIU and IA (current status: completed):

WORKS:

- None

Please note, that SUE “Maxsustrans” has arranged collection points upgrade and rehabilitation (please refer to the package CW5 - #SUE/Maxsustrans/ICB-W5) at own funds and financed these Works by the national currency – Uzbek Sum (current status: the works completed).

SERVICES:

- SUE/Maxsustrans/QCBS-Cons_2 – Landfill Design and Supervision Consultant (current status: shortlisting in progress)

- SUE/Maxsustrans/QCBS-Cons_3 – Corporate Development Consultant (current status: contract negotiated)

- SUE/Maxsustrans/LCS-Cons_5 – Project accounts Audit Services (current status: the original contract completed and amendment 1 signed for further services)

- SUE/Maxsustrans/LCS-Cons_4 – Individual Consultants for IA and PIU (current status: completed):

- Cons_4-IC-1 Project Management and Procurement Specialist (International)

- Cons_4-IC-2 Safeguards Specialist (International)

- Cons_4-IC-3 Financial Management Specialist (National)

- Cons_4-IC-4 Monitoring and Evaluation Specialist (National)

# ENVIRONMENTAL ORGANISATION AND MANAGEMENT

## Organizational & Safeguard Aspects

- PIU Consultants (JV “H.P. Gauff Ingenieure GmbH & Co. KG – JBG- (Germany) and GKW Consult GmbH (Germany) and ENG-INVEST Consulting Ltd. (Uzbekistan)”) were selected through the tender, and the Contract for Project Management, Implementation and Supervision Consultancy Services was signed in January, 2017.

- Under the terms and conditions of the Contract, the PIU Consultants has National Environmental Expert – Ms. Yulya Alekseeva (further replaced by Mr. Sergey Karandaev), who will implement environmental safeguards services.

- International Construction Contractor has not been provided by the TOR and PIU Consultants Contract. It is intended to announce bidding for Construction Contractor in December 2017.

- Additionally, it should be noted that, on June 19, 2017 an advertisement was published to hire Landfill Design and Supervision Consultants. This consulting company will do design works of closing old landfill and establishing of new landfill, and additionally will supervise all construction works related to Landfill establishment.

- The present Quarterly Environmental Monitoring Report covers August-October 2017-time period.

## Project Organization and Stakeholders

- As said above, there are two executing agencies Tashkent City Hokimiyat (City Administration) and State Committee of the Republic of Uzbekistan of Ecology and Environment Protection (SCEEP) responsible for the overall oversight and monitoring of the Project outputs, and also one implementing agency State Unitary Enterprise “MAXSUSTRANS”. PIU was established for assistance in management, planning and implementation of the Project on behalf of SUE “Maxsustrans”.

- Currently the Project organization structure is as follows:

Figure 4: Project Organization Structure

## Agencies Involved in Investment Program Implementation

- The following agencies are involved in implementing the investment program: State Committee of the Republic of Uzbekistan of Ecology and Environment Protection (SCEEP) and Tashkent Hokimiyat (Municipality) are the Executing Agencies (EA). Tashkent Hokimiyat responsible for management, coordination and execution of all activities funded under the loan and has overall responsibility for compliance with loan covenants. SCEEP is responsible for implementation of Part A of the contract – preparation of National Municipal Solid Waste Strategy of city Tashkent. ADB will oversee project sites regularly and give clear instructions for the project sites improvements with regard to environmental safeguards.

- State Unitary Enterprise “Maxsustrans” (Maxsustrans) is the implementing agency (IA), which is responsible for administration, implementation (design, construction and operation) and all day-to-day activities under the loan. An Investment Program Implementation Unit (PIU), is established within the Maxsustrans for Investment Program related functions. The PIU coordinates construction of subprojects, and ensures consistency of approach and performance.

- Maxsustrans hired International PIU Consultants - JV “H.P. Gauff Ingenieure GmbH & Co. KG – JBG- (Germany) and GKW Consult GmbH (Germany) and ENG-INVEST Consulting Ltd. (Uzbekistan). The Leading Company H.P. Gauff has a many-year-long work experience in the field of waste management. According to the Contract terms and conditions, the said Company hired a National Environmental Expert and Social Safeguard and Development Specialist.

## Responsibilities for supervision of environmental matters

- To ensure proper compliance of environmental safeguards, the Environmental Expert of PIU (National Environmental Expert of Project Management, Implementation and Supervision Consultant) will monitor environmental matters and report to the Project Manager who shall advice the Project Director.

- Environmental issues arising from the construction activities should immediately be brought to his attention to coordinate efforts in order to immediately mitigate impacts, protect the environment, and safeguard the health and welfare of the local communities. All these are to be conducted within the framework of the overall construction management and supervision.

## Responsible for carrying out mitigation measures

- During construction stage, implementation of mitigation measures is the construction contractor’s responsibility.

- To ensure implementation of mitigation measures during the construction period, contract clauses for environmental provisions will be part of the civil works contracts. Contractors’ conformity with contract procedures and specifications during construction will be carefully monitored by PIU and Project Management, Implementation and Supervision Consultant.

- The Contractor will have the following obligations:

- To prepare site-specific environmental management plan (SSEMP) for endorsement by the Supervision Consultant and for approval by the Employer prior to the Contractors taking possession of the construction site;

- To employ Environmental Specialist responsible for developing and implementing the SSEMPs for construction phase and for providing the corresponding information to Maxsustrans and Construction Supervision Consultant (CSC);

- Carry out the monitoring and mitigation measures set forth in the IEE/EMP/SSEMP;

- Allocate the budget required to ensure that such measures are carried out;

- Develop waste management plan, contingency plan and other required environmental management plans;

- Agree all environmental management plans with the Maxsustrans PIU;

- Prepare monthly progress reports on SSEMP implementation, which should contain information on the main types of activities carried out during the reporting period, status of any clearances/permits/licenses which are required for carrying out such activities, mitigation measures applied, and any environmental issues that have emerged in relations with suppliers, local authorities, affected communities, et;.

- Coordinate community relations issues through acting as the Contractor’s community relations focal point (proactive community consultation, complaints investigation and grievance resolution).

## Relationships with Contractors, Owner, Lender, etc

- The Construction Supervision Consultant (CSC) is working closely with PIU and the ADB Project Officer. According to the TOR of the CSC, International and National Environmental Specialist (ES) will support the project implementation.

- The responsibilities of the national environment specialist includes:

- Supervise the implementation of the environmental protection and impact mitigating measures by the contractor(s). The project work may only be ordered to start after the review is completed and ES of CSC is satisfied with the environmental arrangement;

- Supervise construction activities to ensure minimum impact on the natural and socioeconomic environment;

- Regularly monitoring the performance of the Contractor(s) environment staff, verifying monitoring methodologies and results. In case the ES of CSC considers that the Contractor(s) environment staff fail to discharge duties or fail to comply with the contractual requirements, instruct the Contractor(s) to replace their environment staff;

- Review of the construction design to ensure compliance with project engineering design and the EMP with regard to environmental protection and impact mitigation;

- Prepare the necessary remedial actions for any unforeseen impacts, and

- Instructing the Contractor(s) to take corrective actions within timeframe as determined by the ES of CSC. If there is breach of contract or strong public complaints on contractor environmental performance, the ES of CSC will order contractor to correct, change or stop the work and reporting to the relevant agencies and the EA;

- Address complaint related with environmental aspect of the project through GRM;

- Supervision of the Contractor(s) activities and ensuring that the requirements in the EMP and contract specifications are fully complied with;

- Instructing the Contractor(s) to take actions to reduce impacts and follow the required EMP procedures in case of non-compliance / discrepancies identified;

- If the contractor discovers cultural relics by chance, the ES of CSC will order site protection and report to the relevant authorities and the EA;

- Monitoring Contractor(s) performance to ensure that they cut trees in strict accordance with the pre-determined area, numbers, and species set out in the permits and comply with wildlife and plant protection requirements during construction;

- Monitoring Contractor(s) compliance with the project grievance redress mechanism.

## Responsible for carrying out monitoring measures

- During construction, Environmental Specialist (ES) of CSC will monitor the construction contractor’s environmental performance.

## Responsible for reporting

- CSC will submit periodic monitoring and implementation reports to PIU, who will take follow-up actions, if necessary. PIU will submit monitoring reports to the Project Director who will then submit to ADB. The annual report is to focus on the progress of implementation of the EMP and Environment Implementation Plan Requirements (EARP) and issues encountered and measures adopted, follow-up actions required, if any, as well as the status of Program compliance with project selection criteria, and relevant loan covenants. PIU will seek clearance for submission and disclosure of the annual environmental monitoring report to ADB.

- During project implementation, the supervision consultants in cooperation with PIU will be required to

- develop an environmental auditing protocol for use during construction, and formulate a detailed monitoring and management plan; and

- regularly supervise the environmental monitoring, and submit quarterly reports based on the monitoring data and laboratory analysis report.

## Third Party Agency for EMP

- No Third Party Agency has been engaged until now. The Employer prefer / suggest latest during the frame work for the Package CW 1 and further an International Environmental Expert should be involved.

## Grievance redresses mechanism (GRM)

- A project-specific grievance redress mechanism (GRM) is established by the EA to provide a transparent mechanism to voice and resolve environmental concerns linked to the project. According to the Decree of President of the Republic of Uzbekistan SUE Maxsustrans established (organized) “People’s Reception Room” in its each district branch in Tashkent city, including one in SUE Maxsustrans building for PIU related queries.  The EA ensures that grievances and complaints are addressed in a timely and satisfactory manner to avoid any potential delays in the establishment of the project. Figure 5 gives the details of the grievance redress mechanism.

Figure 5 Grievance Redress Mechanism

- The PIU has established Grievance Redress Committee (GRC). GRC provides any APs a venue to file complaints and queries on any environmental (or social) aspect related to the project. Grievances can be submitted in writing or orally to the contractor or directly to the PIU / EA contact person. These are properly documented (i.e. indicating the date it was received, details of the complaint and complainant/s) and screened by the designated PCMU safeguard consultant for its veracity and validity. The committee has 15 to 20 days to address and come up with a resolution. Under this GRM, unsatisfied grievances may be able to appeal for a final resolution. This mechanism also does not prevent any AP to approach regulatory agencies to assist and resolve complaints at any stage of the process. In occasions wherein grievances are perceived by the AP to be immediate and urgent; the contractor, EHS officer and PIU on-site supervisor will provide the most accessible and practical solution for a quick resolution of grievances. Such grievances and respective resolutions submitted to the PIU for proper documentation. The PIU contact person is responsible for recording the complaint, the step taken to address grievance, minute of the meetings and preparation of a report for each complaint. Records is kept by the PIU of all grievances received including contact details of AP, date the complaint waste received, nature of grievance, agreed remedial / corrective action and the date this was implemented, and the final outcome in Complaints Log Book kept at the PIU office.

- PIU – responsible person for GRM is the director of PIU, Mr. Rustam Shukurov, tel: +99871 2477923

- EA is SUE Maxsustrans. The responsible person for GRM is Mr. Shukhrat Inogamov, tel: +99871 2473599, email: maxsustrans@inbox.ru

- PCMU Consultant is social and resettlement specialist, Mrs. Maria Malinovskaya, tel: +99871 1508887, email: malinovskaya@almarconsulting.org

- The complaint handling process will be reported to ADB through semi-annual reports. The PIU safeguard consultant will periodically review and record the efficiency and effectiveness of the GRM highlighting the project’s ability to prevent and address grievances.

- There have been no environmental complaints or grievance reported on the sub project till date (October 2017).

Excerpt from Copy of registration book “complaints against social and resettlement”, Akhangaran district, Tashkent- region, January – July 2017

# ENVIRONMENTAL SAFEGUARD COMPLIANCE

- IEE for project was prepared for SUE Maxsustrans in May 2013 and it was published on ADB‘s website. Initial Environmental Examination (IEE) was conducted to determine the current environmental conditions and assess the potential impacts to be brought about by the proposed SLF project. The scope of the IEE is dictated and is consistent to the requirements of the Asian Development Bank (ADB) classified as a Category B project resembling the “OVOS” format used by Goskompriroda in the conduct of an Environmental Impact Assessment (EIA) for Sanitary Landfill (SLF).

## Objectives of the Environmental Management Plan

- The main objectives of an Environmental Management Plan are:

- Ensure that environmental requirements specified in the contract documents are adequately performed.

- Carry out construction and supportive activities in compliance with all relevant Government laws, rules and regulations including environmental laws in force.

- Manage works and operations to prevent or at least minimize adverse impacts on the environment.

- Implement environmental and mitigation measures specified in the contract documents.

- Develop action plan for implementing mitigation measures where and when needed

- Provide safeguard to all workers from any hazard associated with the construction operations and ensure protection of their health

- Ensure protection of the health and welfare of project side communities by minimizing nuisance including pollution.

- Observe the laws and other environmental regulations of the country and liaise with the Engineer and statutory authorities for the smooth and efficient operation to complete the Project.

- With the significant environmental issues identified and evaluated, mitigation measures and monitoring plans were also proposed to prevent or minimize the negative impacts and to enhance positive effects. In order to ensure the proper establishment and operation of the SLF, management and control systems must be implemented which include:

- site management and security

- effective traffic management

- slope stabilization and installation of drainage systems

- installation of environmental control measures (e.g. establishment of a “green” buffer zone, implementation of landfill cover, liner system, leachate collection system and drainage systems) as planned and design (wherein additional control elements shall be implemented whenever deemed necessary or when required)

- regular checks and maintenance on the installed equipment

- strict inspection and effective / immediate processing of waste being received. Proper staff training and practical engineering / operational practices (e.g. orientation and induction training, strict imposition of PPE and tool box talks) complimented with an organized record keeping, performance monitoring and reporting must also be maintained.

- Compliance monitoring and due diligence can be conducted at least on a quarterly basis. Continuous operational improvements as well as employing the best practical environmental options shall also be incorporated into the project.

- It is the responsibility of the PIU therefore to ensure the development of a database that includes a systematic tabulation of process indicators, performance evaluation, maintenance schedules and logbook, and operational control and performance monitoring outputs.

## LARP implementation

- In the proposed project affected area, no group of people maintains a separate cultural and social identity from the mainstream Uzbekistan society that would classify them as ethnic group, ethnic minority or indigenous people as described in ADB SPS, 2009. Therefore, the proposed project has been categorized as a “C” project with regard to indigenous peoples.

- At present the project requires the land acquisition of farmer lands, 30 ha. The negative impact on 34 ha of farmer lands caused by the removal of the irrigation canal is also expected. Process of LARP implementation was stopped. The reason is dissatisfaction of the farm owner with the provided conditions of the compensation held by independent evaluation company. Owner of the farm claims for higher amount of compensation which, at the same time, he cannot justify with documents.

- The current LARP isn’t implemented or ongoing in the necessary requirements and necessities.

There is no physical progress of the LARP implementation at this stage of project implementation. No compensation is paid to the project affected household as a result of dissatisfaction of the farm owner with the provided conditions of the compensation held by independent evaluation company for the affected land plot. He used the designed Grievance redress mechanism and applied to the court. Owner of the leasehold farm claims for higher amount of compensation which, at the same time, he cannot justify with documents. The process of land acquisition and compensation was considered by the local Khokimiyat and Maxsustrans. The rights of ownership of the land plot required for project construction works belongs to affected household ("Shahboz Nuri Ziyo" leasehold farm).

| Indicator | Status | Remarks |
| --- | --- | --- |
| Land acquisition | Not completed | Affected household is unsatisfied with the amount of compensation provided for the lost lands and crops held by independent evaluation company. Owner of the farm claims for higher amount of compensation which, at the same time, he cannot justify with documents. At present the owner of land plot (to be acquired) is affected household. The compensation for lost income is not provided yet. The process of implementation of LARP is not completed. |
| Compensation “land for land” | Not completed |  |
| Compensation for losses (profit) | Not completed |  |
| Compensation for lost income (workers at the farm) | Not completed |  |
| Income restoration | Not completed |  |

Table 1 Status of LARP implementation, October 2017

## ADB Mission

- ADB mission took place from 22-28 August 2017. The main objectives of the Mission were to review and confirm with the Government of Uzbekistan: (i) the key project implementation issues, (ii) project implementation schedule and procurement plan, (iii) contract awards and disbursements (CAD) targets, (iv) loan covenants, and (v) Project Administration Manual (PAM). The Mission visited the sanitary landfill site and waste transfer stations, conducted meetings with the Ministry of Finance (MOF), the Ministry of Economy (MOE), the State Committee of the Republic of Uzbekistan of Ecology and Environment Protection, Tashkent City Hokimiyat (Tashkent Municipality), State Unitary Enterprise “Maxsustrans” (Maxsustrans) and Project Implementation Unit (PIU). A wrap-up meeting with Tashkent Municipality, Maxsustrans, and PIU was held on 28 August 2017.

- The Mission reminded Maxsustrans that it should ensure that the design, construction, and operation and maintenance of the facilities under the project are carried out in accordance with ADB SPS, 2009, applicable laws and regulations of Uzbekistan, and recommendations of the IEE and its EMP, though the civil works have not started yet. PIU advised the Mission that the national environment specialist will be on board by mid-September 2017. Maxsustrans assured the Mission that potential adverse environmental impacts arising from the project are minimized by implementing all mitigation and monitoring measures as presented in the EMP of the IEE. If necessary changes should be made in the project design, the updated IEE will be prepared and all necessary government permits and licenses, including ecological expertise opinion, to construct the sanitary landfill facility will be obtained prior to commencing SLF civil works. Baseline environmental measurements will be carried out by the contractor before commencement of the civil works.

## Communication

- During the reporting period regular meetings and discussions to communicate the project related issues took place with ADB mission, PIU management and environmental team and official authorities.

Communication took place via official letters, emails, phone calls and personal contacts. Regular weekly meetings took place between Environmental specialist and PIU. Various issues were discussed. Particularly the following issues were touched during the reporting period:

- Update on baseline data collection and reporting,

- Regular Monitoring findings,

- Other routine issues.

# Environmental Monitoring

- No baseline monitoring for environmental conditions has been done for proposed project. Baseline environmental measurements will be carried out by the contractor before commencement of the civil works.

- Permanent environmental monitoring will start immediately after the commencement of the civil works by the contractor under the “Solid Waste Management Improvement Project”.

- According to Environmental Monitoring Plan included into IEEs, the following parameters needed to be monitored during the construction stage:

- Landscape Alteration;

- Erosion;

- Water;

- Air and Noise;

- Environmental Health and Safety.

- The EMPs indicated that Contractor would be responsible for conduction visual monitoring of above indicated parameters. No more requirements on environmental monitoring were included in EMP and as following in SSEMP. Instrumental monitoring of quality of environment was not conducted.

## The Environmental Management System, site-specific environmental management plan (SSEMP) and work plans

- SSEMP for the project “Solid Waste Management improvement Project” will be prepared by Environmental Specialist of construction company before commencement of the civil works. SSEMP will be approved by PIU, after which construction company can start construction activities.

## Site Inspections and Audit

- Not yet applicable.

## Non-Compliance Notices

- Not yet applicable.

## Corrective Action Plans

- Not yet applicable.

## Actions taken to reflect the findings of ADB mission

- The semi-annual Safeguards Monitoring Reports for the period of January-July 2017 were posted on Maxsustrans website.

## Consultations and Complaints

Public Awareness Activities:

- No public awareness activities were carried out within the project during the period of August-October 2017.

# CONCLUSIONS AND ACTION PLAN FOR THE NEXT PERIOD

- Establishment of environmental and social team within the PIU was completed as it is an issue of compliance with legal covenants.

- Action plan for the reporting period from November 2017 to March 2018:

| # | Action | Time frame | Responsibility |
| --- | --- | --- | --- |
| 1 | Safeguard Compliance and Monitoring Report (2nd quarterly report) | Q1, 2018 | PIU Consultants National Social Safeguards and Development Specialist |
| 2 | Review the environmental monitoring checklist with regard to current requirements and update as required. | Q1, 2018 | PIU Consultants National Social Safeguards and Development Specialist |
| 3 | Collect and provide the relevant information on environmental indicators to PIU. | Q1, 2018 | PIU Consultants National Social Safeguards and Development Specialist |
| 4 | Other routine issues like unscheduled site visits, follow up of the detected defects, environmental assessment of designs. | Upon the need | PIU Consultants National Social Safeguards and Development Specialist |
| 5 | Reporting on environmental safeguards | Monthly Bi-annual | PIU Consultants National Social Safeguards and Development Specialist |

# Footnotes

Acc. to the President Decree #UP 5024 from 21.04.2017 the State Committee of Uzbekistan for Nature Protection was renamed into the State Committee of the Republic of Uzbekistan of Ecology and Environment Protection (SCEEP)

Excluding USD 314 608.78 interest charges deducted from the loan account by ADB